## Slide 1: A P3D model for fracture growth across multiple elastic layers
Onshore gas Program
Xi ZhangA,B
ACSIRO Energy, Melbourne, VIC 3168, Australia. BOn leave at Institute Of Rock and Soil Mechanics, CAS, Wuhan, China
Notes: Only twenty minutes. 4 minutes for discussion

## Slide 2: CSIRO Australia’s National Science Agency
62% of our people hold university degrees
2000 doctorates
500 masters
Supervising 650 postgraduate students with university partners
Top 1% of global research institutions in 14 of 22 research fields
Top 0.1% in 4 research fields
Locations
55
Budget
$1B
4500
People
Darwin
Alice Springs
Atherton
Townsville 2 sites
Rockhampton
Toowoomba
Gatton
Myall Vale
Narrabri
Mopra
Parkes
Griffith
Belmont
Geelong
Hobart
Sandy Bay
Wodonga
Newcastle
Armidale 2 sites
Adelaide
2 sites
Sydney 5 sites
Canberra 7 sites
Cairns
Irymple
Melbourne 5 sites
Werribee 2 sites
Brisbane
6 sites
Bribie Island
Geraldton 2 sites
Perth
3 sites
Murchison
Established
1926

## Slide 3: Outline
Introduction
Model
Numerical Results
Conclusions

## Slide 4: Walloons Coal at Surat Basin
Pandey and Flottman, 2015
Locations of Walloons Coal Seam Gas Reservoirs
Many untargeted seams are fractured due to vertical growth. (Pandey and Flottmann, SPE, 2015)

## Slide 5: Multilayer Structure and Hydraulic Fracturing
Layered coal seam structures at Surat Basin (Pandey and Flottmann, 2015)
  Thin Walloon coal seams range from 0.2 to 3 m in thickness.
  Inter-burden (non-coal) rock layers are impermeable.
  Large modulus contrasts between coal seams and non-coal rocks.
Hydraulic fracturing technique is used to enhance the permeability of coal seams. For most cases, vertical wells are used.
Coals are fractured. If Slick water is used, the fracture area is spreading, while cross-linked gel is used, fracture is more like a planar fracture. The latter is our concern for the model.
Layer fracture model| Xi Zhang

## Slide 6: Modulus Contrast
If a hydraulic fracture is confined in a layer, low viscosity fluid and low injection rate are used (Kirk-Bounnand et al, 2015). However, this is not suitable to fine-thickness low-permeability coal seams. How to optimize fracture design.
What is the consequence of stress and material property contrasts?
Micro-Seismic events show the fractures are confined by sharp changes of modulus.
Crack deflection to form L or T shaped fractures (Jeffrey et al., 2015, CSIRO

## Slide 7: Fracture Types and Stress Conditions
Special stress conditions for the coal seams that located in
between 400 and 900 m.
Stress along depth from Pandey and Flottmann, 2015
Transition between Reverse and Strike-slip regime.
Upward growth could be arrested by Reverse regime or weak interfaces to form horizontal fractures.
Fracture plane could mainly be vertical for deeper fractures. This is considered by this talk.

## Slide 8: Previous Work and Findings
Modulus contrast can provide a barrier to vertical growth. (Zhang et al. 2007; Gu et al, 2011; …)
Horizontal growth can be generated by weak interfaces and inside a layer. (Gu, et al., 2000, 2008; Gu and Weng, 2011; Jeffrey et al., CSIRO Internal report, 2015)
Discontinuities (Chuprakov et al, 2014; ..)
Complex fluid flow (Weng 1992)
Proppant transports (Dontsov and Peirce, 2014, 2015)
Production and induced stress changes

## Slide 9: Outline
Introduction
Model
Numerical Results
Conclusions

## Slide 10: Multi-Layer P3D Model
Aims: to consider fracture growth into a multiple layer rock and to provide fracture shape and opening.
Cell-based Pseudo-3D fracture model: No Fluid lag +Open mode fractures
Elastic properties and stress contrasts between layers are considered.
Fracture surface contact is considered.
From Zhang et al., IJSS, 2017

## Slide 11: Layer Stresses due to Modulus Contrasts
Stress-strain relations in each layer
The lateral strains across layers are the same.
The resultant stress along the depth should be equal
to the tectonic stress
The governing equations (right) and solve for the strains.
Finally calculate the stresses for each layer.
Tectonic stresses and Overburden stress
Two tectonic stresses
OB stress at the top
Gravity force
(Bourne, 2003)

## Slide 12: Assumptions
The elastic deformation in a cell is plain strain.
The pressure distribution in each cell is uniform
The fluid flow direction is horizontal only. The horizontal flow is described by a mass balance equation.
Layer interfaces are strongly bonded (No interface Fractures).
Fracture propagation occurs in both horizontal and vertical directions by satisfying the LEFM failure criterion.

## Slide 13
Governing Equations
Plane-strain elasticity (only opening is involved)
Fluid flux in horizontal direction (Cubic law)
Mass balance for horizontal flow
(Adachi et al., 2007)

## Slide 14: Validation of Green’s Functions
We calculate Green’s function for multi-layers based on image methods. How to truncate the image series? We use up to five-order images or a section of five layers.
Three-layer problems
E1
E2
2d
2a
d/a=0.1
2a
a/d=0.8
E1
E2

## Slide 15: Moving Fronts
Calculate Stress Intensity factors based on displacements
Crack front movement in both vertical and horizontal directions
When one criterion is met, a new element is added in the corresponding direction for a specific cell.
Vertical Fracture toughness
c highlights cell interaction and needs calibration.
Additional terms are attributed to viscous fluid flows.
e is 0.15 times of cell height.
d is the cell width.
Horizontal Fracture toughness
Notes: Chi for

## Slide 16
We need iteration method to solve elastic deformation in each cell. Normally, use cell-based pressures. Here we use a fluid volume-based optimization method. (Zhang et al., IJSS, 2017)
For given fluid volume of a cell, find the solution.
More stable compared to fluid pressure
Contact problem solved by iterations
Although no theoretical solutions are used, we can solve it cell by cell. So Parallel computing is used.
Solution Method
functional

## Slide 17: Model Verification
Comparison with fully-3D code outcomes and PKN solutions
* ILSA is a planar-3D code for homogeneous solids with stress contrast.
By varying the only-undetermined parameter c in the model to generate close heights to ILSA. Its ranges for six cases are obtained.
KIC=0
KIC=1.5 MPa m0.5
From Zhang et al., JPSE, 2018

## Slide 18: Determine c
Can we apply this relation to more general cases???
0.2
0.28
0.31
0.42
K
c

## Slide 19: Computation Speed and Mesh Sensitivity
Use the left Eq to calculate c.
The results show less mesh sensitivity.
From Zhang et al., JPSE, 2018
Computing time for Fig. 9(a) in the study by Dontsov and Peirce (2015)
on a CSIRO Dell PowerEdge M630 cluster

## Slide 20: Proppant Transport
Fluid mass balance
Proppant transport
where
From Dontsov and Peirce, 2014
unknown

## Slide 21: A solution method for proppant transport
Integrate proppant transport equation along the z-direction
The total particle volume in each cell is obtained by solving the equation. To avoid concentration oscillation, WENO method is used.
In which
=0 at fracture edges.
No discontinuity.
Qx
Qz
Block function is exactly the same as Wang et al. (2018).

## Slide 22: Proppant settling
Assume that particle setting rapidly reaches the steady state in a cell.
Based on the constraint: the total particle in this cell
is known
If some elements have a large concentration, they are assigned to the critical concentration. numerically, rearrangement restarts.

## Slide 23: Outline
Introduction
Model
Numerical Results
Conclusions

## Slide 24: Example 1: Injection Pressure Variations

## Slide 25: Input Data
Mesh used
Perforation layer
Rock
Coal
Fluid
Depth=700m at Z=0, vertical fracture growth
Two closely-spaced seams
Two stress conditions

## Slide 26: Fracture Shape and Opening Contours
42.3 s
99.4 s
162.9 s
Fracture propagates upwards to untargeted seams
The fracture front in the perforation layer stops growth.
Larger opening exists in softer coal seams.

## Slide 27: Varying Injection Pressure
Actual measurement of injection pressure variations
Two different options for calculating c produce similar results.
Use layer-based results below.

## Slide 28: Alternating Vertical and Horizontal Growth
There are two periods when height growth is temporarily arrested. This is caused by softer layers.
The faster height growth rate causes a faster drop in injection pressure.
42.3 s
99.4 s

## Slide 29: Cross-Section Opening near Well
With stress contrast
Confining stress is 6.8 MPa
for all layers
Height is the same at this time instant (t=142 s).
Although opening values depend on stress contrast, the opening shapes are the same for two cases.

## Slide 30: Example 2: in situ Stress Variations

## Slide 31: Input Data
Mesh for a two-coal seam rock body.
Each cross point is an element.
Cell number increases with fracture growth.
Injection point
A weak plane at z=47 stops further upward growth.
The height locations for the coal seam tops and bottoms are (49.3, 49.8) and (68.5, 69.3).
The coal seams have Young’s modulus of 4 GPa, Poisson’s ratio of 0.4, density of 2,000 kg/m3 and fracture toughness of 0.67 MPa.m0.5.
The stiffer rocks have Young’s modulus of 20 GPa, Poisson’s ratio of 0.2, density of 3,000 kg/m3 and fracture toughness of 0.67 MPa.m0.5.
The fracturing fluid is taken as slick water with a viscosity of 0.001 Pa.s and the fluid density of 1,000 kg/m3. The injection rate used in the simulation is 0.04 m3/s.

## Slide 32: Stress Conditions
Use the above equation to calculate stresses based on tectonic stresses.
* Stresses within each layer.
Two tectonic stresses
14 and 21 MPa
sz0= 15, 15, 17 MPa

## Slide 33: Simulation Result – Injection Pressure
The varying trends of injection pressure are the same even in situ stress calculation method is changed.
Pressure tends to reduce at large time. No dominated horizontal fracture growth occurs.
PKN and T-shaped dominant growth modes have different injection pressure responses.

## Slide 34: Overburden Stress changes
* Overburden stress =15, 17 MPa
Fracture lengths in coal seams are shorter.
Upward growth is constrained by the upper coal seam.
Max opening is not in coal seam, but in the rock mass close to interface.

## Slide 35: Example 3: Proppant transport

## Slide 36: Input data
a homogeneous rock with a Young’s modulus E=1 GPa and a Poisson’s ratio n=0.2. Toughness is zero.
The fluid viscosity is 0.1 Pa∙s and the total injection rate Q0=0.01 m3/s.
10 m
Stress conditions:
Pay zone stress (s1)
Upper and lower rocks (s2)
Sand inj rate: 0.5 kg/s Vol% =5%
250
300
650
Time (s)
Inj rate and prop rate
Water density 1000 kg/m^3
Sand density 1500 kg/m^3
Dr=500kg/m^3

## Slide 37: CASE I: Stress difference is 7.2 to 8.0
Particle size =10 microns (ceramic and flour)

## Slide 38: CASE II: Very fine particles
Particle size =10 microns
And stresses are 7.2 and 7.6 MPa

## Slide 39: CASE III: Particle size is increased
Particle size =500 microns (sand)
Stresses are 7.2 and 7.6 MPa

## Slide 40: CASE IV: Proppant injection rate is reduced
Particle size =500 microns
Stresses are 7.2 and 7.6 MPa
Proppant inj rate= 0.05kg/s
Longer fracture

## Slide 41: Outline
Introduction
Model
Numerical Results
Conclusions

## Slide 42: Conclusions
An attempt was made on MLP3D from fracture generation, proppant transport to production for coal seam gas stimulation in multiple thin layers.
Modulus contrasts and stress variations are two important factors. The untargeted seams can be fractured by vertical growth.
Oscillating injection pressure change implies that the horizontal fractures are not dominated.
How is vertical growth limited? Larger stress in coal seams due to strain compatibility can make vertical growth difficult. Proppant gravity effect can do too.

## Slide 43: FRACTURA
Hydraulic fracturing simulation toolkit
CSIRO ENERGY

## Slide 44: Thank you
Onshore Gas program
DR. Xi Zhang (xi.zhang@csiro.au)